## Slide 1
iFAMS v. 6.3 Quant Demo

## Slide 2
Note: Keep GUI file/executable in the same location as the “iFAMS Fun” folder

## Slide 3
Load in MS data as .csv or .txt
Displays chromatogram for extracting MS data across a retention time window (only available in Quant+)
Loads processed spectra and displays additional saved content if processed from iFAMS v6.3
Loads in processing settings from a “batch_params” file
Uses stored processing settings to deconvolve set of MS files or .d files
Saves recent deconvolved spectrum and integrated peaklist
Saves processing settings to a “batch_params” file

## Slide 4
Tools for deconvolving a spectrum using ordinary FT

## Slide 5
Tools for deconvolving a spectrum using STFT which includes the Gabor spectrogram

## Slide 6
Menu for generating calibration curves

## Slide 7
Isotope calculator for checking deconvolution against a theoretical mass distribution based on the analyte’s sequence

## Slide 8
Zoom tool is quite handy for finding signal in the spectrogram. Remember to deselect Zoom to resume drawing boxes on the spectrogram for selecting signal.
These two options can help with replotting spectra within the iFAMS windows.
Saves the iFAMS screen as a PNG, EPS, etc.

## Slide 9
To load a Text or CSV file of MS data for deconvolution and quantitation

## Slide 10
Processed as STFT…
BSA signal
NIST mAb signal

## Slide 11
Adjusting the data domain can help focus the search

## Slide 12
Saves a copy of the truncated MS data as a CSV
Replots all spectra with the original MS domain
After replotting over the new domain, close out the dialog box
The new domain is stored and exported with batch parameters

## Slide 13
Adjusting the STFT parameters can improve signal isolation

## Slide 14
STFT parameters for manual adjustment
Automatic STFT adjustment tools

## Slide 15
Determines pixel dimensions in spectrogram.
A higher number results in flatter and wider pixels (higher frequency resolution)
A lower number results in taller and narrower pixels (higher mass resolution)
Adjusts heat map scale for visualization.
Lower values will dilate red features
Higher values will constrict red features
Determines the number of pixels. The default is ten times the number of data points. Higher values increase the number of pixels which results in a “smoothing” effect on the spectrogram

## Slide 17
Decreases FFT channels to increase mass resolution in the spectrogram at the expense of frequency resolution

## Slide 18
Removing high mass resolution for this example…
We are ready to select signal from the spectrogram
Once selections are started, do not readjust STFT spectrogram parameters

## Slide 19
Entering ion mass works well for isotope resolved signal.
Manually selecting two adjacent signals works well for most types of signal.

## Slide 20
These options are selected by default and are recommended for most cases.
For particularly challenging cases:
The top option adjusts each box when making selections. If deselected, the selections are made with average box shapes positioned about maxima.
The bottom option selects a range a charge states that pass an abundance threshold. If deselected, the range selected will include every possible charge state in the m/z range.

## Slide 21
Fundamental signal for NIST mAb
Select two adjacent fundamental signals:
Draw one box on the spectrogram
“Add Gabor selection” (ctrl + e)
“Save Gabor selection” (ctrl + s)
Repeat 1-3 for adjacent signal

## Slide 22
Inverse FT spectra populate here as selections are made
Press “Go” once two adjacent signals have been selected

## Slide 23
Spectrogram slice (shown in orange) helps with verifying charge state selections

## Slide 24
Suggested number of harmonics is editable (1st harmonic = fundamental)
Individual charge states can be selected from deconvolution
Allows multiple proteins to be processed one at a time

## Slide 25
Stored selections displayed here

## Slide 26
No strong or isolated fundamental frequency

## Slide 27
Zoomed in…
Selecting the near-zero frequency (including the zero frequency)

## Slide 28
Unsatisfactory results…
Selections can be removed to try the search again with different initial parameters, or the selections can be tweaked

## Slide 29
Charge-corrected inverse FT spectra
Combined zero-charge spectrum

## Slide 30
Original charge range zoomed in

## Slide 31
x2
Original charge range -1

## Slide 32
Charge states were originally estimated too low by one
Original charge range +1

## Slide 34
The charge states are now adjusted

## Slide 35
Investigating the high m/z end of the distribution
Cut off about here

## Slide 36
Investigating the low m/z end of the distribution
Cut off about here

## Slide 37
The iFAMS deconvolution corrects each inverse FT spectra by the charge and sums them together for the zero-charge spectrum.
A baseline correction is applied to each combined zero-charge spectrum to account for artifacts that arise from the Gabor selection.

## Slide 41
Parameters for finding peaks to integrate autofill with default or auto-calculated values.
Additional baseline correction options
Charge-corrected inverse FT spectra can be viewed to help interrogate validity of peaks.

## Slide 44
Select files (.csv, .txt, or .d) to be processed with the same parameters. This option will also save the parameters and the data from this current deconvolution.

## Slide 45
Additional data that can be saved from each file processed.
Selecting one of these options will create a new folder within the batch folder.

## Slide 46
Batch folder should be located with the processed file and labeled with the date and batch number.

## Slide 47
Loading one deconvolved spectrum will also display the integration and the charge-corrected inverse FT spectra.
Loading multiple deconvolved spectra will just overlay each combined zero-charge spectrum.
Loading IFFT spectra will display the original MS data and overlay the inverse FT spectra labeled with the assigned charge.

## Slide 48
Overlaying the batched deconvolved spectra…

## Slide 49
BSA internal standard
10 ng/µL

## Slide 50
Cal vs. Conc (ng/uL)
0 = 0
1 = 0.005
2 = 0.01
3 = 0.02
4 = 0.05
5 = 0.1
6 = 0.2
7 = 0.4
8 = 2
9 = 4
10 = 8
11 = 10
NIST mAb calibrant

## Slide 51
Cal vs. Conc (ng/uL)
0 = 0
1 = 0.005
2 = 0.01
3 = 0.02
4 = 0.05
5 = 0.1
6 = 0.2
7 = 0.4
8 = 2
9 = 4
10 = 8
11 = 10
NIST mAb calibrant zoomed in…

## Slide 52
Generating a calibration curve

## Slide 55
(Create Calibration Curve)
Tolerance units can be toggled between Da and ppm.
Signal type can be toggled between peak integration and height.
Curve type can be switched between linear, quadratic, and logistic.
There are also various weighting options.
These options can be adjusted later as well.

## Slide 56
Calibrant masses can be easily toggled

## Slide 57
Internal standard masses can also be easily toggled or turned off entirely

## Slide 58
(Calculate Concentrations)
Unknowns and quality controls can be plotted against the curve to calculate their concentrations.

## Slide 59
Zoomed in on the low concentrations…